## Slide 1
OFFICIAL MANUAL WALKTHROUGH
Manual v1.3.1
SHAKTI Processor & SoC Platform Walkthrough
Complete Chapter-Wise Visual Engineering Guide based on SHAKTI User Manual V1.3.1 RISE Lab, IIT Madras • Swadeshi Microprocessor Challenge (MeitY)
🇮🇳 Swadeshi Initiative
Indigenous open-source production-grade processors developed at IIT Madras, funded by MeitY to create sovereign silicon solutions.
🧩 6 Processor Classes
Full RISC-V roadmap spanning from ultra-low power 32-bit microcontrollers (E-Class) to 64-bit multi-core servers (C-Class & I-Class).
⚡ Complete Ecosystem
Full ecosystem: Bluespec SystemVerilog (BSV) RTL, Vivado bitstreams, Board Support Packages (BSP), FreeRTOS, and OpenOCD GDB debugging.
SHAKTI User Manual v1.3.1 (RISE Lab, IIT Madras) • Module 1 of 12

## Slide 2
CHAPTER 1.1 • PROCESSOR FAMILIES
Page 6-7 (Sec 1.1.1)
E-Class: Embedded & IoT Microcontroller Core
Positioned against ARM Cortex-M series for low-power compute, automotive sensors, and smart meters.
MICROARCHITECTURE SPECIFICATIONS
• Architecture: 32-bit RISC-V In-Order pipeline
• Pipeline Depth: 3-Stage (Fetch → Decode/Execute → Writeback)
• Operating Frequency: < 200 MHz on ASIC silicon; 50 MHz on Artix-7 FPGA
• ISA Support: RV32IMAC (Base Integer, Mul/Div, Atomic, Compressed)
• Privilege Modes: Machine (M) mode and optional User (U) mode
• Physical Protection: PMP (Physical Memory Protection) enabled
• Target Workloads: Motor control, IoT sensor nodes, smart cards, automation
3-STAGE IN-ORDER PIPELINE FLOW
📌 Stage 1: Instruction Fetch (IF)
Program counter generation, Instruction cache lookup or BRAM memory access, 16-bit compressed instruction decompressor.
📌 Stage 2: Decode & Execute (ID / EX)
Instruction decoding, Register file operand read, Integer ALU arithmetic/logic, Branch resolution, Multi-cycle pipelined multiplier/divider.
📌 Stage 3: Memory & Writeback (MEM / WB)
Data cache / peripheral MMIO read/write access, Register file commit, CSR updates, Exception & Interrupt handling.
SHAKTI User Manual v1.3.1 (RISE Lab, IIT Madras) • Module 2 of 12

## Slide 3
CHAPTER 1.1 • PROCESSOR FAMILIES
Page 6-7 (Sec 1.1.2)
C-Class: Mid-Range 64-Bit Controller Core
Industrial 64-bit core running up to 1 GHz, equipped with Sv39 MMU to boot full Linux distributions.
Feature Attribute | SHAKTI E-Class (e32) | SHAKTI C-Class (c64)
Word Size (XLEN) | 32-bit (RV32) | 64-bit (RV64)
Pipeline Structure | 3-Stage In-Order (Fetch, Decode/Exec, WB) | 5-Stage In-Order (Fetch, Decode, Exec, Mem, WB)
Silicon Clock Frequency | < 200 MHz on ASIC | 800 MHz – 1.0 GHz on ASIC
Memory Management (MMU) | Physical Memory Protection (PMP) | Sv39 MMU (Full Virtual Memory for Linux)
Target ARM Equivalent | ARM Cortex-M0+ / M4 | ARM Cortex-A35 / Cortex-A55
Supported Operating Systems | Baremetal, FreeRTOS, Zephyr RTOS | Full Linux, FreeBSD, RTEMS, FreeRTOS
SHAKTI User Manual v1.3.1 (RISE Lab, IIT Madras) • Module 3 of 12

## Slide 4
CHAPTER 2 • BOARD DETAILS & SOCS
Page 9-11 (Sec 2.1)
Development Boards & 3 Reference SoC Flavors
The Swadeshi Microprocessor Challenge supports three official SoCs targeting Digilent Xilinx Artix-7 boards.
PINAKA (e32-a35)
Target: Arty A7-35T FPGA
• Core: E-Class 32-bit (RV32IMAC)
• RAM: 128KB On-Chip BRAM (No DDR)
• Peripherals: 3 UART, 2 SPI, 2 I2C, 6 PWM, 32 GPIO
• Special: Xilinx ADC (XADC) hardware interface
• Use Case: Low cost embedded sensors & motor drives
PARASHU (e32-a100)
Target: Arty A7-100T FPGA
• Core: E-Class 32-bit (RV32IMAC)
• RAM: 256MB DDR3 High-Speed External RAM
• Networking: 10/100 AXI Ethernet Lite MAC
• Peripherals: Full Pinaka I/O set + Ethernet
• Use Case: Networked IoT gateways & buffer-heavy apps
VAJRA (c64-a100)
Target: Arty A7-100T FPGA
• Core: C-Class 64-bit (RV64IMAC)
• RAM: 128MB DDR3 High-Speed External RAM
• Networking: 10/100 AXI Ethernet Lite MAC
• Privilege Modes: Machine, Supervisor, User
• Use Case: Capable of booting full Linux OS kernel
SHAKTI User Manual v1.3.1 (RISE Lab, IIT Madras) • Module 4 of 12

## Slide 5
CHAPTER 3.1 & 3.2 • BOARD SETUP
Page 11-13 (Sec 3.1-3.2)
Hardware Connections & Dual-Channel FTDI Debugger
Single Micro-USB connector (J10) supplies 5V power, JTAG hardware debugging, and UART0 serial console.
FTDI FT2232H DUAL-CHANNEL ROUTING
🔹 Channel A (MPSSE Engine): JTAG Hardware Debugging
Wired to FPGA JTAG pins (TCK, TMS, TDI, TDO). Used directly by OpenOCD to communicate with the RISC-V Debug Module over JTAG, providing hardware breakpoints and stepping without an external pod.
🔹 Channel B (Serial UART): System Console Terminal
Wired directly to the SHAKTI SoC UART0 (TX/RX) pins at 19,200 baud (8N1). Presents a standard virtual COM port (/dev/ttyUSB0 or COMx) on the host PC for console printf output.
SETUP PROCEDURE & VERIFICATION
1. Connect J10 Port: Plug Micro-USB cable into connector J10 on the Arty-7 board and host PC.
2. Verify Power LED: Green LED LD11 turns ON, confirming 5V bus power delivery.
3. Check Linux Device Nodes:
$ ls -l /dev/ttyUSB*
/dev/ttyUSB0 (UART0 Console @ 19,200 baud)
/dev/ttyUSB1 (OpenOCD JTAG MPSSE Engine)
4. Grant Serial Permissions on Host PC:
$ sudo usermod -a -G dialout $USER
$ sudo chmod 666 /dev/ttyUSB*
SHAKTI User Manual v1.3.1 (RISE Lab, IIT Madras) • Module 5 of 12

## Slide 6
CHAPTER 3.3 • FPGA FLASHING
Page 13-19 (Sec 3.3.3-3.3.6)
Programming SHAKTI onto SPI Configuration Memory
Burn the compiled .mcs configuration file into onboard Quad-SPI Flash memory for persistent power-on boot.
VIVADO HARDWARE MANAGER WORKFLOW
1. Open Vivado: Launch Vivado Design Suite 2018.3 or newer.
2. Open Hardware Manager: Click "Open Target" → "Auto Connect".
3. Add Configuration Memory: Right-click FPGA target (xc7a35t or xc7a100t) and select "Add Configuration Memory Device".
4. Select SPI Flash Part Parameters:
• Manufacturer: Spansion (s25fl128sxxxxxx0) or Micron (n25q128-3.3v)
• Density: 128 | Type: spi | Width: x1_x2_x4
5. Program Flash: Select downloaded pinaka.mcs file and click OK.
6. Reload FPGA: Press the board PROG button or power-cycle to boot!
COMMAND-LINE AUTOMATED BUILD & FLASH
# 1. Clone official SP2020 repository:
git clone --recursive https://gitlab.com/shaktiproject/sp2020.git
cd sp2020/e32-a35/
# 2. Complete RTL synthesis & bitstream build:
make generate_verilog generate_boot_files \
ip_build arty_build generate_mcs \
program_mcs JOBS=4
# 3. Direct prebuilt .mcs programming without Vivado build:
# Download prebuilt .mcs from: gitlab.com/shaktiproject/sp2020/-/tree/master/mcs
openocd -f ./shakti-arty.cfg
SHAKTI User Manual v1.3.1 (RISE Lab, IIT Madras) • Module 6 of 12

## Slide 7
CHAPTER 4 • SOC ARCHITECTURE
Page 20-25 (Sec 4.1)
SoC Memory Map & Peripheral Addressing
Unified Memory-Mapped I/O (MMIO) address layout compliant with RISC-V Privileged Architecture v1.10.
Peripheral Block | Base Address Range | Description & Hardware Registers | Target SoCs
Boot ROM | 0x0000_1000 - 0x0001_0FFF | First-stage bootloader, initial stack setup & ASCII boot logo | All SoCs
UART 0 | 0x0001_1300 - 0x0001_1340 | Primary serial console wired to FTDI Micro-USB (19,200 baud) | All SoCs
UART 1 & UART 2 | 0x0001_1400 / 0x0001_1500 | Auxiliary serial communication channels routed to header pins | All SoCs
SPI 0 & SPI 1 | 0x0002_0000 / 0x0002_0100 | Serial Peripheral Interface for Flash memory and external sensors | All SoCs
PWM 0 to PWM 5 | 0x0003_0000 - 0x0003_05FF | 6 independent Pulse Width Modulation channels for motor & LED | All SoCs
GPIO & PinMux | 0x0004_0100 & 0x0004_1500 | 32 General Purpose I/O pins and dynamic pin multiplexing register | All SoCs
CLINT & PLIC | 0x0200_0000 / 0x0C00_0000 | Standard RISC-V timer (mtime/mtimecmp) and Platform Interrupts | All SoCs
Main Memory | 0x8000_0000 - 0x8FFF_FFFF | Pinaka: 128KB BRAM ¦ Parashu: 256MB DDR3 ¦ Vajra: 128MB DDR3 | Specific Target
SHAKTI User Manual v1.3.1 (RISE Lab, IIT Madras) • Module 7 of 12

## Slide 8
CHAPTER 5.1 & 5.2 • SOFTWARE ECOSYSTEM
Page 26-33 (Sec 5.1-5.2)
SHAKTI-SDK Architecture & Toolchain Installation
Modular C/C++ development framework providing Board Support Packages (BSP), drivers, and toolchain setup.
LAYERED SOFTWARE ARCHITECTURE
📦 Application Layer
User C/C++ programs, sensor demos, algorithmic benchmarks
📦 OS / Middleware Layer
FreeRTOS kernel, Zephyr RTOS, Picolibc C standard library
📦 Board Support Package (BSP)
Hardware drivers (UART, I2C, SPI, PWM, GPIO, PinMux, XADC)
📦 Low-Level Architecture
Startup routines, Trap handlers, Linker scripts, RISC-V CSRs
📦 Physical Hardware
Pinaka (Artix-7 35T), Parashu (100T), Vajra (100T)
TOOLCHAIN SETUP COMMANDS
# 1. Install system prerequisites (Ubuntu 18.04/20.04/22.04):
sudo apt-get install autoconf automake autotools-dev curl \
libmpc-dev libmpfr-dev libgmp-dev libusb-1.0-0-dev bc \
gawk build-essential bison flex texinfo gperf libtool \
patchutils zlib1g-dev libftdi1 libftdi1-2 python3-serial
# 2. Clone SHAKTI-SDK & SHAKTI-TOOLS:
git clone https://gitlab.com/shaktiproject/software/shakti-sdk.git
git clone https://gitlab.com/shaktiproject/software/shakti-tools.git
# 3. Build RISC-V Cross Compiler & OpenOCD:
cd shakti-tools && ./setup.sh
export PATH=$PWD/bin:$PWD/openocd/bin:$PATH
SHAKTI User Manual v1.3.1 (RISE Lab, IIT Madras) • Module 8 of 12

## Slide 9
CHAPTER 5.3 • APP DEVELOPMENT
Page 33-35 (Sec 5.3)
Application Development Flow: Adding & Compiling Code
Standard process for adding a new user application, linking with BSP drivers, and generating executable ELF.
4 STEPS TO ADD A NEW APPLICATION
📌 1. Choose Peripheral Directory
Navigate to ./software/examples/XYZ_applns (e.g. uart_applns, gpio_applns, pwm_applns).
📌 2. Create Application Folder & Source
Create a subfolder (e.g. hello_uart/) and write hello_uart.c using BSP driver APIs (#include "uart.h").
📌 3. Create Local Makefile
Define application targets, source file lists, and compilation flags adhering to the SDK structure.
📌 4. Register in Master Makefile
Add hello_uart to the target list in ./software/examples/Makefile to enable top-level building.
BUILD COMMANDS & ARTIFACTS
# 1. List all registered applications:
make list_applns
# 2. Build for Pinaka SoC (RV32IMAC):
make software PROGRAM=hello_uart TARGET=pinaka
# 3. Build for Parashu SoC (RV32IMAC + DDR):
make software PROGRAM=hello_uart TARGET=parashu
# 4. Build for Vajra SoC (RV64IMAC):
make software PROGRAM=hello_uart TARGET=vajra
# Output Artifacts in output/ directory:
• app.elf (Executable and Linkable Format binary)
• app.dump (Complete RISC-V assembly disassembly)
• app.hex (Memory initialization hex for simulation)
SHAKTI User Manual v1.3.1 (RISE Lab, IIT Madras) • Module 9 of 12

## Slide 10
CHAPTER 5.4 • DEBUGGING WORKFLOW
Page 35-37 (Sec 5.4)
Interactive Debugging Mode: 3-Terminal Workflow
Live non-intrusive debugging using OpenOCD GDB server and RISC-V GNU Debugger over USB JTAG.
TERMINAL 1: UART CONSOLE
# Displays serial printf outputs:
sudo miniterm.py /dev/ttyUSB0 19200
Settings:
• Baud Rate: 19,200 baud
• Data bits: 8
• Parity: None
• Stop bits: 1 (8N1)
TERMINAL 2: OPENOCD SERVER
# Launch OpenOCD JTAG Server:
cd ./bsp/third_party/artix7_35t
sudo openocd -f ftdi.cfg
Status:
• Initialises FT2232H MPSSE
• Discovers RISC-V Tap (hart 0)
• Opens GDB Server on :3333
• Opens Telnet on :4444
TERMINAL 3: RISC-V GDB
# Start RISC-V GDB Client:
riscv32-unknown-elf-gdb
(gdb) target remote localhost:3333
(gdb) file output/hello_uart.elf
(gdb) load
(gdb) b main
(gdb) continue
SHAKTI User Manual v1.3.1 (RISE Lab, IIT Madras) • Module 10 of 12

## Slide 11
CHAPTER 5.5 • DEPLOYMENT MODE
Page 37-38 (Sec 5.5)
Running in Standalone Mode: Autonomous Power-On Boot
The application binary is flashed into SPI Flash memory, enabling independent execution on board power-on.
DEBUG MODE VS. STANDALONE MODE
📌 Debug Mode (Development)
Requires Host PC running OpenOCD and GDB over JTAG. Binary is temporarily loaded into volatile RAM. Once power is turned off, application is lost. Best for iterative development.
📌 Standalone Mode (Production)
Binary is permanently burned into non-volatile Quad-SPI Flash memory. On board reset or power-up, the hardware bootloader autonomously copies the code from Flash into RAM and executes. Best for deployed field products.
FLASH UPLOAD & HARDWARE BOOT SEQUENCE
# One-Shot Upload Command in SHAKTI-SDK:
cd shakti-sdk
make upload PROGRAM=hello_uart TARGET=pinaka
Hardware Execution Sequence on Reset:
1. Hardware Reset: CPU resets PC to BootROM address (0x0000_1000).
2. BootROM Execution: Boot code initializes memory controllers.
3. SPI Flash Read: Boot loader reads user binary from SPI Flash.
4. Copy to RAM: Payload copied into main RAM (0x8000_0000).
5. Jump & Run: CPU jumps to RAM entry point and begins user code!
SHAKTI User Manual v1.3.1 (RISE Lab, IIT Madras) • Module 11 of 12

## Slide 12
APPENDIX A & B • HARDWARE INTERFACING
Page 38-46 (Appendix A-B)
Arduino Pin Mapping & Dynamic PinMux Architecture
Standard Arduino Uno R3 header compatibility with 2-bit dynamic hardware multiplexing registers.
PINMUX 2-BIT REGISTER LOGIC (0x0004_1500)
⚡ Bits = 00 (Default)
Configures physical pin as standard General Purpose I/O (GPIO).
⚡ Bits = 01 (Serial / SPI)
Routes pin to serial peripherals: UART1, UART2, or SPI1 (TX/RX/MOSI/MISO).
⚡ Bits = 10 (PWM Mode)
Routes pin to Pulse Width Modulation output (PWM0 to PWM5).
⚡ Bits = 11 (Reserved)
Undefined hardware behavior; reserved for future expansions.
DYNAMIC PINMUX PROGRAMMING IN C
#include <stdint.h>
#define PINMUX_REG (*(volatile uint32_t *)0x00041500)
// Example: Configure Arduino Pin IO3 (CK_IO[3]):
// Bits [7:6] control CK_IO[3] routing:
// 1. Enable PWM0 output on Pin IO3:
PINMUX_REG &= ~(0b11 << 6); // Clear bits 7:6
PINMUX_REG |= (0b10 << 6); // Set bits 7:6 to 10 (PWM0)
// 2. Switch Pin IO3 to UART2 TX dynamically:
PINMUX_REG &= ~(0b11 << 6); // Clear bits 7:6
PINMUX_REG |= (0b01 << 6); // Set bits 7:6 to 01 (UART2 TX)
// 3. Revert Pin IO3 back to standard GPIO:
PINMUX_REG &= ~(0b11 << 6); // Set bits 7:6 to 00 (GPIO)
SHAKTI User Manual v1.3.1 (RISE Lab, IIT Madras) • Module 12 of 12